## Slide 1: Hydrologic modeling is commonly used to forecast the impacts of proposed actions on future water resource conditions. Models are simplified mathematical representations of complex hydrogeologic systems. Therefore, it is inevitable that predictions made with these models will have some degree of error / uncertainty. The art and science of hydrologic modeling is based on a modelers ability to identify those complexities that can be simplified without causing unacceptable errors / uncertainties in the forecasts of interest. The first step toward identifying potential sources of error is to understand how reality is represented in a model and how a model is molded to fit reality. This occurs, generally, in two steps: conceptualization and parameterization. To conceptualize a model the modeler decides which processes are relevant, at which scales, and how they will be represented in the model including: dimensionality; hydrogeologic structure; degree of transience, numerical solution details; and – if absolutely necessary – chemistry. To parameterize a model, the modeler decides how to represent the physical (OK, and chemical) properties of the system in the context of the mathematical representation of that system. For example, the wonderous complexity of the internal structure of a porous medium becomes two numbers: porosity and permeability - in a stretch, permeability may differ horizontally and vertically. Simultaneously, the complex structure of a braided river channel becomes geometric blocks of uniform properties – or, abstract geostatistical Rorschach Tests of spatially correlated blobs. Those material properties that do not affect the processes that the modeler has chosen to include are irrelevant to the model. Calibration (aka parameter estimation) is generally limited to changing the value of parameters to make the mathematical incarnation of a conceptual model fit data – recognizing that those data also suffer from ‘measurement error’ – a term that hides a multitude of sins. In practice, the boundary conditions – and to a greater extent, the structure – of a model are only changed if a good fit cannot be achieved through parameter fiddling adjustment.

## Slide 2: Given all of this, how can a modeler assess the error / uncertainty of their predictions. Error – aka bias – can only be assessed in retrospect, when it’s too late to be useful. The only way to determine if a model’s predictions are biased is to compare them to reality. This is exactly what occurs during model calibration – parameters are adjusted to reduce the mismatch between a model and all existing data. Uncertainty – aka variance – can be thought of as answering the question: if many models give acceptably good fits to the existing data, how different are their forecasts? Note here that you will get a different question if you make different forecasts. The ‘closer’ the forecasts are to the existing data – in space, time, driving conditions, and type – the more likely that they will have small variance. Of course, forecasts for conditions that are not too different than the current, observed conditions may not require a model in the first place. This brings up a key point – models should be created and assessed in the context of specific forecasts. Those forecasts should inform the allowable simplifications and define the metric of model variance. Enough words already, let’s look at a flow chart! The following outlines three levels of model uncertainty that can (should?) be considered when using models to support water resources decisions.

## Slide 3: Current Reality
Conceptual Model
Forecast
Mathematical Model
Future Reality
Hydrology for 100. What Is A Model?
* The choice of which forecasts are important should inform model construction.

## Slide 4: Current Reality
Conceptual Model
Forecast
Data
Calibration of Solution Space
Future Reality
Mathematical Model
Data … A Way to Ruin A Perfectly Good Model
* Subsurface data are expensive, therefore limited, and difficult to collect, therefore prone to errors.
The set of parameters that link a model to reality form ‘parameter space’. The predictions that are compared with observations during calibration are only sensitive to the values of some of those parameters – the ‘solution space’. We assume – because we don’t have an option, really – that improving the ability of a model to match the existing data will improve its ability to forecast the future. This is probably a perfect example of necessary, but not sufficient.

## Slide 5: Current Reality
Conceptual Model
Forecast
Data
Calibration of Solution Space
Future Reality
Mathematical Model
Null Space
Equally Likely
Forecast with Uncertainty
Past Performance Does Not Guarantee Future Results
* Because these models are equally likely, a simple Wisdom of the Crowd averaging can be used to improve the forecast.
Parameters whose values can be changed without changing the fit of a model to the data form the ‘null space’. Forecasts may be sensitivity to some of these parameters. Therefore, by varying these parameters we can form multiple equally good-fitting (equally likely) models that make a range of forecasts. This is the first level of forecast uncertainty estimation.

## Slide 6: Current Reality
Conceptual Model
Forecast
Data
Calibration of Solution Space
Future Reality
Mathematical Model
Null Space
Likelihoods
Forecast with Uncertainty
Likelihoods
Not Bloody Likely!
* Likelihoods can weight the forecasts of different models to make more robust decisions with quantified uncertainties.
Many models might have very similar goodness of fit to the (imperfect and sparse) data. It seems equally foolhardy to choose one model or to ignore goodness of fit. Remember that likelihood means ‘relatively likely to be accurate among the models considered’ – it is generally based on goodness of fit to the data. The second level of forecast uncertainty considers models of different likelihood, each perturbed in the null space.

## Slide 7: Current Reality
Conceptual Model
Forecast
Data
Calibration of Solution Space
Future Reality
Mathematical Model
Null Space
Likelihoods
Forecast with Uncertainty
Likelihoods
Trouble
Here Comes Trouble
* Advocacy models intentionally introduce stakeholder bias into model conceptualization. How could that be OK?
Parameter estimation and null space perturbation can be automated. So far, model conceptualization cannot. As a result, conceptual errors are often ignored – giving rise to hydrologic ‘surprise’. Fool me once …. The third level of forecast error analysis requires a modeler to layer model conceptualization onto parameter estimation. Currently, we only do this under duress.